## Slide 1: A novel TCAM management for IPv6 routing table update 一個新的為TCAM設計的 IPv6路由表更新演算法
Design of High Performance Internet Routers
(高效能網際網路路由器設計)
Notes: 1

## Slide 2: Outline
Introduction
Related Works
  PLO_OPT
  CAO_OPT
Proposed Scheme
Performance Evaluation
Conclusion
Notes: 2017/5/10
CSIE CIAL Lab
2

## Slide 3: Introduction(1/5)
Router
  The primary function of routers is to forward packets toward their final destinations.
What is IP address lookup?
  In order to find the destination of each packet, the packet’s destination address lookuped in routing table.
  IP lookup speed is the major bottlenecks faced by internet routers.
packet
action
Router
routing
table

## Slide 4: Introduction(2/5)
208.12.21.20
Longest match
Router
1
2
3
4
0
208.12.21.20
A prefix is an aggregation of IP addresses: 208.12.21/24 = {208.12.21.0, … , 208.12.21.255}
Longest prefix match problem.
Routing table

## Slide 5: Introduction(3/5)
What is TCAM?
  Ternary content-addressable memory (TCAM) is widely used as lookup engine for commercial router or network device
  Two major properties leading TCAM to find the longest match quickly :
    TCAM allows a fully parallel search of the routing table.
    Each cell in a TCAM can take three logic states: “0”, “1”, or don’t-care “X”.

## Slide 6: Three TCAM organizations

## Slide 7: Introduction(4/5)
0: disable
1: enable
1
0
0
1
1
0
0
TCAM
Global mask
1
1
1
1
1
1
Longest prefix match using TCAM
SRAM
0x000
0x001
0x010
0x011
0x100
0x101
Port A
Port B
Port C
Port D
Port C
Port B
0x010
Priority
Encoder
Prefix
Memory location
0x000
0x001
0x010
0x011
0x100
0x101
Decreasing Length
1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
0
X
X
X
X
X
X
X
X
X
X
X
X
0 1 1 0 1 1
Case : Search key is an IP address
Case : Search key is a prefix
0 1 1 0 X X
0
1
1
1
0
0
1
1
1
0
0
1
Port C
len1= 5
0x001
len0
len1
len2
len3
len4
len5

## Slide 8: Introduction(5/5)
In order to ensure the LPM is correct, the prefix length ordering in TCAM should always be maintained when update is taking place.
32-bit prefixes
31-bit prefixes
30-bit prefixes
9-bit prefixes
.
.
.
8-bit prefixes
1
M-1
TCAM
Prefix length ordering in TCAM
Free space

## Slide 9: Outline
Introduction
Related Works
  PLO_OPT
  CAO_OPT
Proposed Scheme
Performance Evaluation
Conclusion
Notes: 2017/5/10
CSIE CIAL Lab
9

## Slide 10: Related Work (1/7)
Update Scheme
  Prefix-length ordering (PLO) constraint:
Two prefixes of the same length don’t need to be in any specific order.
    PLO_OPT
  Chain-ancestor ordering (CAO) constraint
There’s an ordering constraint between two prefixes if and only if one is a prefix of the other (enclosure).
    CAO_OPT
Notes: The NFA build in FPGA is a pipelined architecture.
It also called Brute-force approach.
Each state of transition chain is a pipeline stage.
In case of a match or mismatch, it shifts only one position to the right.
For example, if we have pattern “abc”, and input string “123abc”.
In each cycle, we have one input character.
In first three cycle, we don’t match any character.
In forth cycle, we have matched “a”, and hold the match signal to first register.
In the last two cycle, they also match ”b” and “c”.
The pattern has input matched this pattern.

## Slide 11: Related Work (2/7)
PLO_OPT
  Divide all prefixes into different groups
  by length.
  Two prefixes in the same group can be
  in any order.
  keep all the unused entries in the center
  of the TCAM.
  The worst-case number of memory
  operations per update is L/2.
  L is the number of distinct lengths
.
.
.
.
.
.
32-bit prefixes
31-bit prefixes
21-bit prefixes
20-bit prefixes
9-bit prefixes
free space
8-bit prefixes
1
24
25
.
.
.
.
.
.

## Slide 12: Related Work (3/7)
Prefix:208.12.63.82/32
Prefix:208.12.82/20
32-bit prefixes
31-bit prefixes
21-bit prefixes
20-bit prefixes
9-bit prefixes
free space
8-bit prefixes
1
24
25
PLO_OPT Insertion
PLO_OPT Deletion
.
.
.
.
.
.
Free space start boundary +1
Free space end boundary +1

## Slide 13: Related Work (4/9)
CAO_OPT
  PLO constraint is more restrictive, the constraint can be relaxed to only overlapping prefixes.
  Prefixes that lie on the same chain of the trie need to be ordered.
Q1
Q4
Q2
Q3
free space
Q1
Q4
Q2
Q3

## Slide 14: Related Work (5/9)
CAO_OPT
  A logical inverted trie can be superimposed on
  the prefixes stored in the TCAM.
  Only prefixes in the same path have ordering
  constraint.
  The CAO_OPT algorithm also keeps the empty
  space in the center of the TCAM.
  For every prefix, the longest chain that this
  prefix belongs to should be split around the
  empty space as equally as possible.
  The worst-case number of memory
  operations per update is D/2. where
  D is the max length of any chain in the trie.
Q1
Q4
Q2
Q3
Maximal chain
free space

## Slide 15: Related Work (6/9)
Notation statement
  LC(p)
  len(LC(p))
  rootpath(p)
  ancestors of p
  children of p
  hcld(p)
  HCN(p)
free space
p
LC(p)
hcld(p)
Children of p
Ancestors of p

## Slide 16: Related Work (7/9)
  Moving prefixes on HCN(q)
  Moving prefixes on LC(q)
Case2:
When the prefix to be inserted
is below the free space .
CAO_OPT Insertion
Case1:
When the prefix to be inserted
is above the free space .
free space
LC(q)
Insert
q here
free space
LC(q)
HCN(q)
Insert
q here

## Slide 17: Related Work (8/9)
CAO_OPT Deletion
  It works on the chain that has prefix p adjacent to the free space.
free space
q
delete

## Slide 18: Related Work (9/9)
Shortcoming to shift above schemes for IPv6
  PLO:
    There are 128 different length of prefix in IPv6. Therefore, the worst case and average case of cost to shift the prefix stored in TCAM growth extremely.
  CAO:
    CAO need to maintain the additional trie structure using SRAM.
    Each update cost O(L) time to modify the data store in the trie.
    In order to reorder the chain sequence, the router needs to hold-on for prefix update. It will cause packet drop rate increase when needing more memory access times.

## Slide 19: Outline
Introduction
Related Works
  PLO_OPT
  CAO_OPT
Proposed Scheme
Performance Evaluation
Conclusion
Notes: 2017/5/10
CSIE CIAL Lab
19

## Slide 20: Proposed Scheme (1/13)
Our method using level to group prefixes
Define level
H
D
E
B
1
8
TCAM
A
C
G
F
Level 1
Level 2
Level 3
Level 4
B
A
D
G
C
E
F
H
B
H
G
A
D
E
F
C
Level 1
Level 2
Level 3
Level 4

## Slide 21: Proposed Scheme (2/13)
Three important properties of the prefix enclosure relationship
  All the prefixes in the same level are disjoint.
  The prefix containing any one of the level i prefixes must be stored in level (i+1) or higher level.
  The highest level in IPv4 and IPv6 routing table is 7 and 11.

## Slide 22: Proposed Scheme (3/13)
Other details about our method
  We put free space between level 1 and level 2
    More than 98% prefixes stored in level 1
    and level 2.
M+1
TCAM
Free space
Level 1
Level 2
Level M
1
.
.
 | AS2.0 | AS1221 | AS6447 | V6Gene1 | V6Gene2
Level 1 | 2808 | 867 | 2870 | 115709 | 123279
Level 2 | 184 | 62 | 205 | 2875 | 2770
Level 3 | 8 | 3 | 13 | 1048 | 794
Level 4 | 1 | 1 | 2 | 563 | 428
Level 5 | 0 | 0 | 0 | 269 | 183
Level 6 | 0 | 0 | 0 | 169 | 87
Level 7 | 0 | 0 | 0 | 130 | 71
Level 8 | 0 | 0 | 0 | 57 | 39
Level 9 | 0 | 0 | 0 | 23 | 27
Level 10 | 0 | 0 | 0 | 12 | 11
Level 11 | 0 | 0 | 0 | 6 | 8

## Slide 23: Proposed Scheme (4/13)
  We adds additional bits named “Level index”
  in TCAM. To avoid spending cost to maintain
  the trie structure.
    The length of level index is log2L bits
  Every level is associated with a link list called free_list to record its empty entries of this level.
Level index
M+1
TCAM
Level 1
Level 2
Level M
1
Free space
1
2
M
.
.
0
pos
NULL
pos
pos
The free list of level 3

## Slide 24: Proposed Scheme (5/13)
free
free
free
free
free
free
free
free
free
free
000
000
000
000
000
000
000
000
000
000
TCAM
Level index
Initial
A : 1100
A : 1100001
B : 1***001
3-bits level index
B : 1***
0x0000
0x0001
0x0010
0x0011
0x0100
0x0101
0x0110
0x0111
0x1000
0x1001
B cover A
Level 1
Level 2
B : 1***010
C : 11**001
C : 11**
C : 11**010
B : 1***011
Level 3
Level 2
D : 1101001
D : 1101
Level 1
B cover C
Disjoint
Level 3
Level 4
Level 1
Level 2
level index+1
B
H
G
A
D
E
F
C
Level 1
Level 2
Level 3
Level 4
(A)1100
free
free
free
free
free
free
free
free
free
001
000
000
000
000
000
000
000
000
000
TCAM
Level index
(A)1100
free
free
free
free
free
free
free
free
(B)1XXX
001
000
000
000
000
000
000
000
000
010
TCAM
Level index
C cover A
(A)1100
free
free
free
free
free
free
free
free
(C)11XX
001
000
000
000
000
000
000
000
000
010
TCAM
Level index
(A)1100
free
free
free
free
free
free
free
(C)11XX
001
000
000
000
000
000
000
000
010
TCAM
Level index
(A)1100
free
free
free
free
free
free
free
(C)11XX
(B)1XXX
001
000
000
000
000
000
000
000
010
011
TCAM
Level index
(A)1100
(D)1101
free
free
free
free
free
free
(C)11XX
(B)1XXX
001
001
000
000
000
000
000
000
010
011
TCAM
Level index
(A)1100
(D)1101
(E)1110
(H)1001
free
free
(G)100X
(F)111X
(C)11XX
(B)1XXX
001
001
001
001
000
000
010
010
011
100
TCAM
Level index

## Slide 25: Proposed Scheme (6/13)
Insertion
  Case 1: no ancestor, n children
No action
Insert q
Layer-1 prefixes
Layer-2 prefixes
Layer-3 prefixes
Layer-4 prefixes
Layer-N-1 prefixes
Layer-N prefixes
Log2N-bits index
128-bits IPv6 prefixes
1
2
3
4
N
N-1
Free space
Ex1: 1 child
If free_list[2] == NULL
If free_list[2] != NULL
Insert q
C1
q
C1
Notes: The differences between the traditional NFA and our proposed scheme are as follows.
First, the number of transition edge in each state will not increasing with the number of input characters.
Second, the number of state is quite fewer than traditional NFA
/*
In transition edge, our proposed scheme is only one as the number of input characters increase.
In number of state, our scheme becomes approximate divide by n of the traditional NFA.
*/

## Slide 26: Proposed Scheme (7/13)
  Case 1: no ancestor, n children
Layer-1 prefixes
Layer-2 prefixes
Layer-3 prefixes
Layer-4 prefixes
Layer-N prefixes
Log2N-bits index
128-bits IPv6 prefixes
1
2
3
4
N
Free space
No action
No action
No action
Layer-N-1 prefixes
N-1
Insert q
If free_list[4] != NULL
Ex2: 3 children
If free_list[4] == NULL
Insert q
C3
C2
C1
q
C2
C1
C3
Notes: The differences between the traditional NFA and our proposed scheme are as follows.
First, the number of transition edge in each state will not increasing with the number of input characters.
Second, the number of state is quite fewer than traditional NFA
/*
In transition edge, our proposed scheme is only one as the number of input characters increase.
In number of state, our scheme becomes approximate divide by n of the traditional NFA.
*/

## Slide 27: Proposed Scheme (8/13)
  Case 2: m ancestors, no children
Layer-1 prefixes
Layer-2 prefixes
Layer-3 prefixes
Layer-4 prefixes
Layer-N prefixes
Log2N-bits index
128-bits IPv6 prefixes
1
2
3
4
Free space
Replace A1 by q
Insert A1
Layer-N-1 prefixes
N-1
Insert A1
If free_list[2] != NULL
Ex1: 1 ancestors
If free_list[2] == NULL
Find A1
q
A1
Notes: The differences between the traditional NFA and our proposed scheme are as follows.
First, the number of transition edge in each state will not increasing with the number of input characters.
Second, the number of state is quite fewer than traditional NFA
/*
In transition edge, our proposed scheme is only one as the number of input characters increase.
In number of state, our scheme becomes approximate divide by n of the traditional NFA.
*/

## Slide 28: Proposed Scheme (9/13)
  Case 2: m ancestors, no children
Layer-1 prefixes
Layer-2 prefixes
Layer-3 prefixes
Layer-4 prefixes
Layer-N prefixes
Log2N-bits index
128-bits IPv6 prefixes
1
2
3
4
N
Free space
Replace A3 by q
A3  A2
Layer-N-1 prefixes
N-1
Insert A1
If free_list[4] != NULL
Ex2: 3 ancestors
Find A3
Find A2
Find A1
A2  A1
If free_list[4] == NULL
Insert A1
A1
A3
A2
q
Notes: Here, we implement the proposed architecture in FPGA.
We design a Pre-Process Module (PPM) which can handle the operations needed in the pre-processing state.
We define three cases in order to control in our PPM.
The case 1 is called “Normal case”, the input string exactly matches the pattern “Processor” at each clock cycle.
For initial cycle, the packet payload will match “Pr”.
In the second and three cycles, the “oc” and “es” have been matched in this case.
The case 2 is called “Shift Case” which may have a 1 or more-byte shift in pattern.
And the case 3 is called “No Match Case” which does not match any string in initial cycle.

## Slide 29: Proposed Scheme (10/13)
  Case 3: m ancestors, n children
Layer-1 prefixes
Layer-2 prefixes
Layer-3 prefixes
Layer-4 prefixes
Layer-5 prefixes
Layer-N prefixes
Log2N-bits index
128-bits IPv6 prefixes
1
2
3
4
5
N
Free space
No action
q instead A1
No action
Layer-N-1 prefixes
N-1
A1 instead A2
A2 instead A3
AN-4 instead AN-3
Insert AN-3
Insert AN-3
If free_list[N] != NULL
Ex1: N-3 ancestors, 2 children
If free_list[N] == NULL
C2
C1
Find A1
AN-3
A1
An-2
q
C1
C2

## Slide 30: Proposed Scheme (11/13)
Deletion
  Case 1: no parent
Ex: Delete (B)
1XXX
(A)1100
(D)1101
(E)1110
(H)1001
free
free
(G)110X
(F)111X
(C)11XX
(B)1XXX
001
001
001
001
000
000
010
010
011
100
TCAM
Level index
0x0000
0x0001
0x0010
0x0011
0x0100
0x0101
0x0110
0x0111
0x1000
0x1001
NULL
0x1001
The free list of level 4
No parent, delete simply
Level 3
Level 4
Level 1
Level 2
Exactly Match
B
H
G
A
D
E
F
C
Level 1
Level 2
Level 3
Level 4

## Slide 31: Proposed Scheme (12/13)
  Case 2: has parent, has sibling
(A)1100
(D)1101
(E)1110
(H)100X
free
free
(G)110X
(F)111X
(C)11XX
Empty entry
001
001
001
001
000
000
010
010
011
100
TCAM
Level index
0x0000
0x0001
0x0010
0x0011
0x0100
0x0101
0x0110
0x0111
0x1000
0x1001
Ex: Delete (G)
level index+1
Exactly Match
Level 3
Level 4
Level 1
Level 2
Finding parent
110X011
Has parent
P
S
(C)’s Difference set
(C)
(G)
level index-1
Has sibling
(F)
110X
has sibling, delete simply
NULL
0x0110
The free list of level 2
Finding sibling
111X010
111X
H
G
A
D
E
F
C
Level 1
Level 2
Level 3
Level 4

## Slide 32: Proposed Scheme (13/13)
  Case 3: has parent, no sibling
(A)1100
(D)1101
(E)1110
(H)100X
free
free
Empty entry
(F)111X
(C)11XX
Empty entry
0001
0001
0001
0001
0000
0000
0010
0010
0011
0100
TCAM
Level index
0x0000
0x0001
0x0010
0x0011
0x0100
0x0101
0x0110
0x0111
0x1000
0x1001
Level 3
Level 4
Level 1
Level 2
Ex: Delete (E)
1110
level index-1
No sibling
level index+1
P
1111001
1110010
Has parent
Exactly match
NULL
0x1000
The free list of level 3
Finding sibling
Finding parent
(A)1100
(D)1101
(F)111X
(H)100X
free
free
Empty entry
(F)111X
(C)11XX
Empty entry
0001
0001
0001
0001
0000
0000
0010
0010
0011
0100
TCAM
Level index
0x0000
0x0001
0x0010
0x0011
0x0100
0x0101
0x0110
0x0111
0x1000
0x1001
Level 3
Level 4
Level 1
Level 2
P
F instead E
Finding grandparent
111X010
1111
Has grandparent
GP
C instead F
(A)1100
(D)1101
(F)111X
(H)100X
free
free
Empty entry
(C)11XX
Empty entry
Empty entry
0001
0001
0001
0001
0000
0000
0010
0010
0011
0100
TCAM
Level index
0x0000
0x0001
0x0010
0x0011
0x0100
0x0101
0x0110
0x0111
0x1000
0x1001
Level 3
Level 4
Level 1
Level 2
111X
111X011
H
A
D
E
F
C
Level 1
Level 2
Level 3
Level 4

## Slide 33: Outline
Introduction
Related Works
  PLO_OPT
  CAO_OPT
Proposed Scheme
Performance Evaluation
Conclusion
Notes: 2017/5/10
CSIE CIAL Lab
33

## Slide 34: Performance Evaluation (1/10)
National Cheng Kung University CSIE Computer & Internet Architecture Lab
34
We first collect IPv6 routing table AS2.0, AS1221, AS6447 from http://bgp.potaroo.net/.
We also use IPv6 prefix generator from [1] to generate two routing tables named V6Gene1, V6Gene2.
[1] Kai Zheng, Bin Liu, “V6Gene: AScalable IPv6 Prefix Generaotr for Route Lookup Algorithm Benchmark”

## Slide 35: Performance Evaluation (2/10)
Prefixes’ distribution
Notes: Well, we develop our hardware architecture in Xilinx ten version
and The simulation for each pattern set was synthesized,
placed, and routed on the Virtex5 chip.
The pattern sets are selected from the OpenSource software ClamAV which it has over fifty thousand pattern sets.
Our architecture can be evaluate by following metric.
The higher Area Density and the higher speed in one chip, it has the better performance in this architecture.

## Slide 36: Performance Evaluation (3/10)
Worst case analysis in theory
  PLO_OPT : ⌈L/2⌉
  In IPv6, the min. length is 16 and the max. length is 128.
  =>⌈(128-15)/2⌉ = 57.
  CAO_OPT : ⌈D/2⌉
  In IPv6, the D is less than 11.
  =>⌈11/2⌉ = 6.
  Proposed scheme : 1+2*(D-2)
  =>1+2*(11-2)=19.

## Slide 37: Performance Evaluation (4/10)
Performance of insertion
 | PLO_OPT |  | CAO_OPT |  | Proposed | 
 | # of Lookup | # of Write | # of Lookup | # of Write | # of Lookup | # of Write
AS2.0 | 0 | 7.204 | 0 | 1.206 | 1.068 | 1.029
AS1221 | 0 | 5.426 | 0 | 1.189 | 1.076 | 1.039
AS6447 | 0 | 7.498 | 0 | 1.254 | 1.077 | 1.037
V6Gene1 | 0 | 10.837 | 0 | 1.407 | 1.084 | 1.079
V6Gene2 | 0 | 10.560 | 0 | 1.368 | 1.062 | 1.057
 | Worst case |  | Worst case |  | Worst case | 
AS2.0 | 0 | 22 | 0 | 3 | 4 | 6
AS1221 | 0 | 18 | 0 | 2 | 4 | 5
AS6447 | 0 | 22 | 0 | 3 | 4 | 4
V6Gene1 | 0 | 25 | 0 | 6 | 11 | 19
V6Gene2 | 0 | 25 | 0 | 5 | 11 | 18

## Slide 38: Performance Evaluation (5/10)
National Cheng Kung University CSIE Computer & Internet Architecture Lab
38
Performance of deletion
 | PLO_OPT |  | CAO_OPT |  | Proposed | 
 | # of Lookup | # of Write | # of Lookup | # of Write | # of Lookup | # of Write
AS2.0 | 1 | 9.220 | 0 | 1.164 | 3.689 | 1.064
AS1221 | 1 | 7.558 | 0 | 1.144 | 3.787 | 1.044
AS6447 | 1 | 9.709 | 0 | 1.236 | 3.277 | 1.058
V6Gene1 | 1 | 11.915 | 0 | 1.371 | 2.991 | 1.064
V6Gene2 | 1 | 11.474 | 0 | 1.363 | 2.762 | 1.053
 | Worst case |  | Worst case |  | Worst case | 
AS2.0 | 1 | 17 | 0 | 3 | 20 | 3
AS1221 | 1 | 13 | 0 | 3 | 36 | 4
AS6447 | 1 | 11 | 0 | 3 | 22 | 3
V6Gene1 | 1 | 25 | 0 | 5 | 50 | 9
V6Gene2 | 1 | 26 | 0 | 5 | 86 | 11

## Slide 39: Performance Evaluation (6/10)
To quantify the performance, We introduce the following TCAM hardware functions:
  The TCAM search process is locked during the update process.
  The TCAM memory width is 144 bits.
  The TCAM has a sustained search rate of 360 million lookups per second.
  Writing a prefix into TCAM takes three clock cycle.
  Disable takes one clock cycle.

## Slide 40: Performance Evaluation (7/10)
Chart: Average clock cycle per insertion operation.
| AS2.0 | AS1221 | AS6447 | V6Gene1 | V6Gene2
PLO_OPT | 21.612 | 16.278 | 22.467 | 32.511 | 31.68
CAO_OPT | 3.618 | 3.567 | 3.762 | 4.221 | 4.104
Proposed | 4.115 | 4.193 | 4.188 | 4.321 | 4.233

## Slide 41: Performance Evaluation (8/10)
Chart: Average clock cycle per deletionion operation.
| AS2.0 | AS1221 | AS6447 | V6Gene1 | V6Gene2
PLO_OPT | 28.66 | 23.674 | 30.127 | 36.745 | 35.422
CAO_OPT | 3.492 | 3.432 | 3.708 | 4.113 | 4.089
Proposed | 6.881 | 6.919 | 6.451 | 6.183 | 5.921

## Slide 42: Performance Evaluation (9/10)
The comparison of clock cycle per second between Search and update
Operation | Search | Update | 
# of operation per second | 320,000,000 | 2,000 | 
# of clock cycle per operation | 1 | Lookup | Write
 |  | 1 | 3
Total clock cycle per second | 320,000,000 | 4374 | 6312

## Slide 43: Performance Evaluation (10/10)
Memory cost
 | AS2.0 | AS1221 | AS6447 | V6Gene1 | V6Gene2
SRAM cost of CAO_OPT (Mbyte) | 93.813 | 29.186 | 96.594 | 3777.027 | 3990.375
SRAM cost of Proposed scheme (Mbyte) | 0.031 | 0.031 | 0.031 | 0.059 | 0.059

## Slide 44: Outline
Introduction
Related Works
  PLO_OPT
  CAO_OPT
Proposed Scheme
Performance Evaluation
Conclusion
Notes: 2017/5/10
CSIE CIAL Lab
44

## Slide 45: Conclusion
We proposed an algorithm to manage the TCAM such that incremental update times remain small in average case.
This algorithm can update TCAM without maintain a tries structure.
This scheme can update the TCAM with less SRAM cost and less memory access time.
Notes: In this paper, we proposed a novel pre-process based pattern matching architecture, and implemented it in FPGA.
The simulation results show that the proposed architecture performs better than the exist approaches that also are based on Brute- Force scheme, in terms of the throughput and the slice utilization.
The advantage is that the proposed architecture has a higher slice utilization and a lower hardware complexity.

## Slide 46
Thanks for your attention.
Notes: 46