## Slide 1: Interest Flooding Attack and Countermeasures in Named Data Networking
Authors: Alexander Afanasyev, Priya Mahadevany, Ilya Moiseenko, Ersin Uzuny, Lixia Zhang
Publisher: IFIP Networking, 2013
(International Federation for Information Processing)
Presenter: Chia-Yi, Chu
Date: 2013/11/27

## Slide 2: Outline
Introduction
NDN Overview
Interest Flooding Attacks in NDN
Interest Flooding Mitigation Methods
Evaluation of Interest Flooding Mitigation Methods

## Slide 3: Introduction (1/1)
Provides 3 mitigation algorithms to mitigate Interest flooding
Interest flooding
  malicious users can attack the network by sending an excessive number of Interests. Since each Interest consumes resources at intermediate routers as it is routed through the network, an excessive number of Interests can congest the network and exhaust a router’s memory.

## Slide 4: NDN Overview (1/2)
A receiver-driven, data-centric communication protocol
Communications in NDN are performed using two distinct types of packets
  Interest and Data.
Both types of packets carry a name
  which uniquely identifies a piece of content that can be carried in one Data packet.
content name is composed of one or more variable-length components and be delimited by “/”.
  youtube video would look like: “/youtube/videos/0F8YdlkKO9A/0”.

## Slide 5: NDN Overview (2/2)
NDN routers maintains three major data structures:
  Pending Interest Table (PIT)
    holds all “not yet satisfied” Interests that have been sent upstream towards potential data sources.
  Forwarding Interest Base (FIB)
    maps name prefixes to one or multiple physical network interfaces, specifying directions where Interests can be forwarded..
  Content Store (CS)
    temporarily buffers Data packets

## Slide 6: Interest Flooding Attacks in NDN (1/4)
Interest packets in NDN are routed through the network based on content name prefixes and consume memory resources at intermediate routers.
An attacker or a set of distributed attackers can inject excessive number of Interests in an attempt to overload the network and cause service disruptions for legitimate users
A large volume of such malicious Interests can disrupt service quality in NDN network in two ways: create network congestion and exhaust resources on routers.

## Slide 7: Interest Flooding Attacks in NDN (2/4)

## Slide 8: Interest Flooding Attacks in NDN (3/4)
if the data producer is the exclusive owner of “/foo/bar” namespace, both router B and the data producer would receive all Interests for “/foo/bar/...” that cannot be otherwise satisfied from in-network caches.
An excessive amount of malicious Interests can lead to exhaustion of a router’s memory
  NDN routers maintain per-packet states for each forwarded Interes

## Slide 9: Interest Flooding Mitigation Methods (1/15)
Naïve solution
  restrict the number of Interests forwarded through the network.
Simple implementation technique
  To limit the number of forwarded Interests out of each interface based on the physical capacity of the corresponding interface.
  a slight modification of the well-known Token Bucket algorithm

## Slide 10: Interest Flooding Mitigation Methods (2/15)
  routers can keep track of the amount of data requested that can fully utilize the downstream link
  once the link capacity limit has been reached, they no longer forward new incoming Interests.
  the number of tokens
    the pending Interest Limit
    Delay: the expected time for the Interest to be satisfied
    Data packet size: the size of the returning Data packet.

## Slide 11: Interest Flooding Mitigation Methods (3/15)
  Drawbacks
    result in underutilization of the network
      not all Interests will result in a Data packet
    can nourish DDoS attacks
      If a router has utilized all its tokens to forward malicious Interests, it can no longer forward incoming Interests from legitimate users till the pending malicious Interests start to expire
  Solution
    impose a per interface fairness

## Slide 12: Interest Flooding Mitigation Methods (4/15)
Token bucket with per interface fairness
  extend the Pending Interest Table
  to support flagging of Interests that cannot be immediately forwarded and implement hierarchical queues for each interface
  not actually store a packet, but merely a bi-directional pointer to the existing PIT entry.

## Slide 13: Interest Flooding Mitigation Methods (5/15)

## Slide 14: Interest Flooding Mitigation Methods (6/15)

## Slide 15: Interest Flooding Mitigation Methods (7/15)
Token bucket with per interface fairness
  Drawback
    still admits a relatively large number of Interests from malicious users
    it drops both legitimate and malicious Interests
      attempts to ensure that each interface does not forward more than its fair share of Interests
  Solution
    be able to detect and differentiate to some extent malicious requests from legitimate ones.

## Slide 16: Interest Flooding Mitigation Methods (8/15)
Intelligent attack mitigation
  Routers can proactively maintain up-to-date statistics of Interest satisfaction ratios
    number of forwarded versus number of satisfied Interests
  use these statistics to determine whether an incoming Interest should be forwarded or dropped.
  use the standard exponentially weighted moving average, performed once a second with coefficient , approximately corresponding to a 30-second averaging window.

## Slide 17: Interest Flooding Mitigation Methods (9/15)

## Slide 18: Interest Flooding Mitigation Methods (10/15)

## Slide 19: Interest Flooding Mitigation Methods (11/15)
Satisfaction-based Interest acceptance
  use the Interest satisfaction ratio as a direct probability for accepting (forwarding) or rejecting an incoming Interest
  Parameter
    ensures that the probabilistic model is not enforced when the volume of Interests arriving at a particular interface is small.
  Drawback
    the probability of legitimate Interests being forwarded decreases rapidly as the number of hops between the content requester and producer grows

## Slide 20: Interest Flooding Mitigation Methods (12/15)

## Slide 21: Interest Flooding Mitigation Methods (13/15)
Satisfaction-based pushback
  enable and enforce explicit Interest limit for each incoming interface, where the value of the limit depends directly on the interface’s Interest satisfaction ratio.
  Announce these limits to their downstream neighbors
    Any Interest forwarded from the downstream router is allowed to get through, resulting in genuine Interest satisfaction statistics.

## Slide 22: Interest Flooding Mitigation Methods (14/15)

## Slide 23: Interest Flooding Mitigation Methods (15/15)

## Slide 24: Evaluation of Interest Flooding Mitigation Methods (1/13)
Use the open-source ndnSIM package
  implements NDN protocol stack for NS-3 network simulator
token bucket with per interface fairness
satisfaction-based Interest acceptance
satisfaction-based pushback
To quantify the effectiveness of algorithms
  percentage of satisfied Interests for legitimate users.
  A high percentage of user-expressed Interests are satisfied even while the network is under attack

## Slide 25: Evaluation of Interest Flooding Mitigation Methods (2/13)
Simulations on two different network topologies
  Smaller binary tree topology
  Larger ISP-like topology
The percentage of attackers in the network
  Ranged from 6% attackers to over 50% attackers
Delay
  binary tree topology: 80ms
  ISP-like topology: 330ms
Data size
  1100 bytes

## Slide 26: Evaluation of Interest Flooding Mitigation Methods (3/13)
Small-scale evaluations
  There are 16 end users
    both legitimate and attackers
  Each expressing Interests that are routed towards a single data producer
    placed at the root of the tree.
  Bandwidth of 10 Mbps
  Randomized propagation delay ranging from 1 to 10 ms.

## Slide 27: Evaluation of Interest Flooding Mitigation Methods (4/13)

## Slide 28: Evaluation of Interest Flooding Mitigation Methods (5/13)
Effectiveness of the three mitigation algorithms
  Perform 10 independent simulation runs
  7 client nodes to represent adversaries, 9 client nodes represent legitimate users
    where randomly choose
  10-minute attack window
    Total simulation time was 30 minutes

## Slide 29: Evaluation of Interest Flooding Mitigation Methods (6/13)

## Slide 30: Evaluation of Interest Flooding Mitigation Methods (7/13)
Network reaction to varying number of attackers
  vary the percentage of attackers in the topology from 6% to over 50%.
  as the number of attackers increases, the number of legitimate users decreases
  All other parameters and experimental setup are consistent with the previous experiment

## Slide 31: Evaluation of Interest Flooding Mitigation Methods (8/13)

## Slide 32: Evaluation of Interest Flooding Mitigation Methods (9/13)
Large scale simulations
  based on a modified version of Rocketfuel’s AT&T topology
  extracted the largest connected component
    comprising of 562 nodes
  separated the nodes into three categories
    Clients
      Having degree less than four
    Gateways
      directly connected to clients
    Backbones
      the remaining nodes

## Slide 33: Evaluation of Interest Flooding Mitigation Methods (10/13)

## Slide 34: Evaluation of Interest Flooding Mitigation Methods (11/13)
  Assigned bandwidth and delay values to links based on their type

## Slide 35: Evaluation of Interest Flooding Mitigation Methods (12/13)
  placing the data producer at both a gateway node as well as backbone node
  fixed the number of malicious nodes at approximately 40%
    140 out of 344 client nodes in the topology
  the attack duration spanning a 5-minute interval.

## Slide 36: Evaluation of Interest Flooding Mitigation Methods (13/13)